## Slide 1
Rescue-feet
Gesture Controlled Hexapod with Live stream for rescue operations
Team 8: Archit Sharma, Sai Pranay, Samyu Kamtam

## Slide 2
Project Overview
  Six-legged (18 DOF) locomotion & biologically inspired gait
  Gesture control for remote and convenient operation
  Live stream for teleoperation

## Slide 3
  Enhanced mobility
  Remote controlled operation
  Stability and redundancy
  Real time video streaming
  User-friendly
  Modular & scalable design
Advantages
  Complexity (Design and control)
  Cost
  Energy consumption
  Connectivity issue
  Payload limitations
Disadvantages

## Slide 4
System architecture
Gesture control - Propeller
Gesture control for
navigation using flex sensor
and Memsic accelerometer
Hexapod
Gait calculation for
servo control
Live stream
Picam live video capture
WiFi
Rasperry pi
WiFi

## Slide 5
Hexapod
  Servo: The servo motors receive PWM signals from the I2C-based driver to perform precise joint movements.
  I2C: I2C communication connects the Raspberry Pi to the servo driver for synchronized multi-servo control.
  Power distribution:
    A buck converter steps down 8.3V to 6V to safely distribute power to all 18 servo motors.
    The Raspberry Pi is powered by stepping down 8.3V to 5V using a buck converter to ensure stable and safe operation.

## Slide 6
Rasperry Pi 3b
  OS: Raspbian 64 bit
  used for servo control and camera live stream
Hexapod circuit diagram

## Slide 7
Kinematics

## Slide 8
Gesture control
  Cogs for Performance:
    Multiple cogs on the Propeller read flex sensor and MX2125 accelerometer values while simultaneously encoding and transmitting data to the laptop.
  Propeller Specs & Sensors:
    8-core Parallax Propeller enables true parallel processing.
    Each cog has 2KB RAM for fast local tasks.
    Interfaced with MX2125 MEMS accelerometer and flex sensors for gesture input.

## Slide 9
Movement | Flex 1 (*18) | Flex 2 (*9) | X (*3) | Y (*1) | Encoded value | Final value
Idle | 0 | 0 | 1 | 1 | 4 | 1
Front | 1 | 0 | 1 | 1 | 22 | 2
Front right | 1 | 0 | 0 | 1 | 19 | 3
Front left | 1 | 0 | 2 | 1 | 25 | 4
Back | 0 | 1 | 1 | 1 | 13 | 5
Back right | 0 | 1 | 0 | 1 | 10 | 6
Back left | 0 | 1 | 2 | 1 | 16 | 7
Bounce | 0 | 0 | 1 | 0 | 3 | 8
Kill | 1 | 1 | 1 | 1 | 31 | 9
Encoder logic
State = flex1*18 + flex2*9 + x*3 + y

## Slide 10
Live video stream
Basic object detection algorithm that decodes MJPEG that is streamed and displays the live video overlaid with detections using YOLO algorithm.
person

## Slide 11
Conclusion
  Revolutionize Search and Rescue operations
  Enhances disaster response
  Scalable
  Has versatile applications
  User centric design with gesture based control
  Challenging with respect to system complexity and energy efficiency

## Slide 12
Thank you
  https://www.raspberrypi.com/documentation/computers/camera_software.html#advanced-rpicam-apps
  https://www.youtube.com/watch?v=qs3KhLDUBmk
  https://github.com/shillehbean/youtubep2/blob/main/stream_usb_camera.py
  https://randomnerdtutorials.com/raspberry-pi-mjpeg-streaming-web-server-picamera2/